## Slide 1: Part ii: Multidimensional filter
Larissa Driemeier
Thiago Martins

## Slide 2
Stationary robots (SRs):
They are the manipulators and industrial robots. The base is fixed, and the robot has an open kinematic chain, mainly with an end-effector. In general, they are automated, programmable and with many degrees of freedom. As an example, to position the tool mounted on the end of the robot at any place and at any angle requires six degrees of freedom.

## Slide 3
Mobile robots (MRs):
Controlled by software, use sensors and other technologies to understand its surroundings
and move through the environment. They have ability to move autonomously, with enough intelligence to react and make decisions. They can be land-based, air-based, water-based, hybrid...

## Slide 5
The sensor is not perfect. A reading of 10.0 may correspond to positions 10.4 or 9.6. However, it is very unlikely to correspond to a position of 25.

## Slide 6
velocity
position
Some state that might be true
Unlikely Very likely
We don't know what the actual position and velocity are, but there are a whole range of possible combinations of position and velocity that could be true... some of them are more likely than others.

## Slide 7: Why?
What are the advantages of programming robots probabilistically, when compared to other approaches that do not explicitly represent uncertainty?
Our central conjecture is nothing less than the following:
A robot that carries a sense of its own uncertainty and acts accordingly is superior to one that does not.

## Slide 8: Pre-class review

## Slide 9: Estado
State , can be thought of as a collection of all aspects of the robot and its environment that can impact the future.
A state will be called complete if it is the best predictor of the future . Despite the stochasticity of robot environments, no variable prior to can influence the stochastic evolution of future states.
Discrete temporal processes that meet these conditions are commonly known as Markov chains.
Notes: , a menos que essa dependência seja mediada pelo estado 𝒙_𝑡
The variables regarding the robot itself include its pose, which comprises its location and orientation relative to a global coordinate frame; configuration of the robot’s actuators, such as the joints of robotic manipulators; robot velocity and the velocities of its joints; whether or not its sensors are functioning correctly; the level of battery charge for a battery-powered robots..

## Slide 10: STATE
Discrete temporal processes that meet these conditions are commonly known as Markov chains.
The input is also typically called the control (or action, or the control input).
The measurement , available from sensors.
Notes: , a menos que essa dependência seja mediada pelo estado 𝒙_𝑡
The variables regarding the robot itself include its pose, which comprises its location and orientation relative to a global coordinate frame; configuration of the robot’s actuators, such as the joints of robotic manipulators; robot velocity and the velocities of its joints; whether or not its sensors are functioning correctly; the level of battery charge for a battery-powered robots..

## Slide 12: Let's understand through examples...
Consider a grid containing black and white cells. The arrows indicate that the grid boundaries are cyclic.
Our robot is moving around the grid according to our commands Our command: [[0,1]]
Although we try to command it, the robot has a will of its own, following our orders only 50% of the time, while the other 50% of the time it remains stationary.
Our sensor, on the other hand, correctly detects the color of the ground our robot is on 80% of the time.
Initially, we believe the probability of the robot being in a black cell is twice as high as the probability of it being in a white cell.
[0,0] | [0,1] | 
[1,0] |  | 
  stationary
  right
  left
  down
  up
0.125 0.125 0.125
0.125 0.0625 0.0625
0.125 0.125 0.125

## Slide 13: [0,1]: right
[0,0] | [0,1] | 
[1,0] |  | 
The prediction state is based on a process model. Our process model is defined according to the probability that the robot will move according to our commands.
  stationary
  right
  left
  down
  up
[1,0] | [1,1]
0.125 0.0625
[1,0] | [1,1]
0.5x0.125+0.5x0.0625
0.09375 0.09375
Looking only for these cells
0.125 0.125 0.125
0.09375 0.09375 0.0625
0.125 0.125 0.125

## Slide 14: Sensor: ‘W’
[0,0] | [0,1] | 
[1,0] |  | 
  stationary
  right
  left
  down
  up
Looking only for these cells
[1,0] | [1,1]
[1,0] | [1,1]
0.09375 0.09375
0.09375x0.2 = 0.01875 (/0.29375 = 0.0638)
0.09375x0.8=0.075 (/0.29375 = 0.25532)
0.01875 0.25532
0.08511 0.08511 0.08511
0.06383 0.025532 0.17021
0.08511 0.08511 0.08511

## Slide 15: P
0.08511 0.08511 0.08511
0.06383 0.025532 0.17021
0.08511 0.08511 0.08511

## Slide 16: NORMAL distribution
The probability density function of a normal distribution is given by:
where is the random variable.
  The normal distribution is characterized by two parameters: the mean and the variance .
Notes: Um ponto importante a ser observado, e que eu destaco sempre, é que os modelos preditivos simples geralmente são os modelos mais utilizados, devido ao fato de poderem ser explicados e bem compreendidos. Agora, para adicionar a este ponto; a distribuição normal é simples e, portanto, sua simplicidade a torna extremamente popular.
The coefficient in front, 1/(𝜎√2𝜋), is a constant that does not depend on x; hence, we can think of it as simply a “normalization factor” used to ensure that integral over –inf to +inf = 1.

## Slide 17: the product of the gaussians are gaussians

## Slide 18: the sum of the gaussians are also gaussians...

## Slide 19: Multivariate Gaussian Distribution
The multivariate normal distribution is a multidimensional generalization of the univariate normal distribution. It is useful for analyzing the relationship between 𝑛 multiple normally distributed variables. The multivariate normal distribution is given by
is an -dimensional vector
is the -dimensional mean vector,
is the covariance matrix, and is the determinant of

## Slide 20: example

## Slide 27
Velocity variance
Average
Position variance
velocity
position
Some state that might be true
Unlikely Very likely
velocity
position

## Slide 28: KALMAN FILTER
To begin with, the Kalman Filter is a linear, unbiased estimator that uses a predictor/corrector process to estimate the state given a sequence of measurements.
This means that the overall process involves predicting the state and then correcting it based on the difference between that prediction and the observed measurement. The question becomes how to update the state prediction with the observed measurement, such that the resulting state estimate is:
  a linear combination of the predicted state and the observed measurement
  have an error with zero mean (unbiased).

## Slide 29
Suppose the robot moves along the horizontal axis – a situation that helps us illustrate the Kalman filter algorithm for a simplistic one-dimensional localization scenario.

## Slide 30
The prediction about the robot's location is given by a normal distribution, where the predicted position is centered on the peak of the Gaussian.

## Slide 31
The robot queries its sensor about its location and returns a measurement that is centered on the peak of the bold Gaussian and the Gaussian width corresponds to the uncertainty in the measurement.

## Slide 32
Combining the measurement result with the process produces the bold Gaussian. The mean of this belief is between the two original means, and its radius of uncertainty is smaller than both contributing Gaussians.

## Slide 33
Next, the robot moves to the right. Its uncertainty increases, corresponding to the Gaussian shown in bold.

## Slide 34
Then the robot receives a second measurement illustrated by the Gaussian in bold.

## Slide 35
The combination again leads to the posterior response…

## Slide 36
Correction
Prediction
Measurement
Estimate
t
Prediction
(motion model)
Measurement
(observation model)
Estimate
t+1
PDF
With uncertainty

## Slide 37
Correction
Prediction
Measurement
Estimate
t
Prediction
(motion model)
Measurement
(observation model)
Estimate
t+1
PDF
With uncertainty
Predict
Use the process model to predict the state at the next time step.
Adjust belief to account for uncertainty in the prediction..

## Slide 38
Correction
Prediction
Measurement
Estimate
t
Prediction
(motion model)
Measurement
(observation model)
Estimate
t+1
PDF
With uncertainty
Update
Get a measurement and its accuracy;
Calculate the residual between the estimated state and the measurement;
Calculate gain based on relative accuracy between measurement and prediction;
Set the state between prediction and measurement based on gain;
Update belief in the state based on measurement certainty.

## Slide 39: Tracking
def compute_robot_data(z_var, process_var, count=1, dt=1.):
"returns track, measurements 1D ndarrays"
x, vel = 10., 3.
z_std = math.sqrt(z_var)
p_std = math.sqrt(process_var)
xs, zs = [], []
for _ in range(count):
v = vel + (randn() * p_std)
x += v*dt
xs.append(x)
zs.append(x + randn() * z_std)
return np.array(xs), np.array(zs)
Initial position and velocity
Standard deviation for
measurement and process
Generation of
real positions
Data stored in xs
Generation of
measurements.
Data stored in zs

## Slide 40
xs,zs = compute_robot_data(z_var=1, process_var=10, count=100, dt=0.1)

## Slide 41
State transition function
is the true state of our system
measurement
related to control.
input vector.
Observation matrix
Gaussian Noise
Measurement noise and process noise are statistically independent (uncorrelated) and
Uncertainty in the measurement
Uncertainty in the process

## Slide 42
is the a priori predicted state vector, which is predicted without knowing the current measurement .
When is given, the posterior state can be calculated.
Kalman gain
State transition function
is the true state of our system
measurement
related to control.
input vector.
Observation matrix
Gaussian Noise

## Slide 43: Predict E update
(Process model)
MEASUREMENT
RESIDUAL
PRIOR
POSTERIOR ,
NEW POSTERIOR
TIME
STATE
PREDICTION

## Slide 45: PREDICTION STEP
The process model is applied
Uncertainty increases

## Slide 46: Multidimensional Prediction
We design the state (x,P), the process (F,Q) and the control (B,u)

## Slide 47: State variables
State variables can be either observed variables – measured directly by a sensor, or hidden variables – inferred from observed variables.
For our robot tracking problem, the sensor just reads the position, so the position is observed and the speed is hidden.

## Slide 48: STATE COVARIANCE
Position and velocity are correlated. But how correlated are they to the robot? No idea!
As we will see, the filter calculates this for us. We can therefore initialize the covariances to zero. Of course, if we know the covariances, we should use them.
If we are quite uncertain about the initial position.
Top speed for our robot is around , so in the absence of any other information about the velocity we can set

## Slide 49: Modelo de Processo
We assume that the robot's speed stays constant between predictions.
Of course, this is not exactly true, but as long as the velocity doesn’t change too much during each prediction, you will see that the filter performs very well

## Slide 50
from filterpy.kalman import predict
x = np.array([10.0, 3.0])
P = np.diag([500, 1])
F = np.array([[1, dt], [0, 1]])
x, P = predict(x=x, P=P, F=F, Q=0)
print('x =', x)
dt = 0.1
x = np.array([10.0, 3.0])
P = np.diag([500, 1])
F = np.array([[1, dt], [0, 1]])
Q=0 # Q is the process noise
x = F @ x
P = F @ P @ F.T + Q
print('x =', x)
x = [10.3 3.]
Qual será a resposta???
Implementation of the prediction step
Using Filterpy

## Slide 51
for _ in range(4):
x, P = predict(x=x, P=P, F=F, Q=0)
print('x =', x)
x = [10.6 3. ]
x = [10.9 3. ]
x = [11.2 3. ]
x = [11.5 3. ]
print(P)
[[5.0025e+02 5.0000e-01]
[5.0000e-01 1.0000e+00]]
Off-diagonal elements became non-zero - the Kalman filter detected a correlation between position and velocity!
Inspection of the diagonals shows us that the position variance has increased. We performed five prediction steps without measurements and our uncertainty increased. The speed variance has not changed.
See what happens in the Notebook!

## Slide 52: Process noise 𝑸
However, the speed is affected by a number of unknown factors and as a consequence the cruise control is unable to maintain a perfectly constant speed.
There are many unknown factors – hills, curves, changes in the coefficient of drag, the effects of wind, rain, and so on…
A car is driving on the road with the cruise control on and must travel at a constant speed.
PMR3408

## Slide 53: Process noise 𝑸
In general, the design of the 𝑸 matrix is among the most difficult aspects of Kalman filter design.
We are trying to model the noise of something we have little information about.
PMR3408

## Slide 54: Process noise 𝑸
In general, the design of the 𝑸 matrix is among the most difficult aspects of Kalman filter design. We are trying to model the noise of something we have little information about.
  If 𝑸 is too small, the filter will become overconfident in its prediction model and diverge from the actual solution.
  If 𝑸 is too large, the filter will be unduly influenced by noise in the measurements and will perform suboptimally.
In practice, we spend a lot of time running simulations and evaluating the data collected to try to select an appropriate value for 𝑸.

## Slide 55: Piecewise white noise matrix
The model assumes that the highest-order term (acceleration) remains constant over a given time interval and is uncorrelated across different time intervals. In other words, there is a discontinuous jump in acceleration at each time step.
𝚪 is the noise gain of the system and constant 𝜔 is the piecewise acceleration

## Slide 56: Piecewise white noise matrix
The model assumes that the highest-order term (acceleration) remains constant over a given time interval and is uncorrelated across different time intervals. In other words, there is a discontinuous jump in acceleration at each time step.
Over a time interval, the change in velocity will be , and the change in position will be , such that

## Slide 57: Matrix

## Slide 58: Matrix

## Slide 59: Matriz

## Slide 60: Matrix
A good rule of thumb is to set σa close to Δa to Δa , where Δa is the maximum change that the acceleration can undergo between sampling periods.
In practice, we choose a number, run simulations on the data, and choose a value that works well.

## Slide 61
from filterpy.common import Q_discrete_white_noise
Q = Q_discrete_white_noise(dim=2, dt=1., var=2.)
print(Q)
var = 2.
dt = 1
Tvector = np.array([[dt**2 / 2], [dt]])
Q = Tvector * var * Tvector.T
print(Q)
Import the function Q_discrete_white_noise function to calculate the matrix .
Call the function
Calcula a matriz
[[0.5 1. ]
[1. 2. ]]

## Slide 62
B = 0.
u = 0
dt = 0.3
F = np.array([[1, dt], [0, 1]])
x = np.array([10.0, 4.5])
P = np.diag([500, 500])
x, P = predict(x, P, F, Q, B, u)
print('x =', x)
print('P =', P)
Our robot does not listen to us...
Call the function
x = [11.35 4.5 ]
P = [[545.5875 151.175 ]
[151.175 502.35 ]]

## Slide 63
In the next step, we should try to adjust our guess. We have the predicted state and now, the sensor reading.
Sensor 1
Sensor 2

## Slide 64: UPDATE STEP
Importance of gain

## Slide 65: UPDATE
Covariance, measurement noise
Kalman gain
We will define the measurement (z,R) and the observation matrix H
residue
Observation matrix
We define so that has the same unit as the measurement.

## Slide 66: matrix
For this problem we have a sensor that measures the position

## Slide 67: matrix
Estimation error is the difference between the true state and the estimated state
Covariance matrix
A miracle happened here...
See the miracle in the Notebook!

## Slide 68: gain
The Kalman gain is determined by minimizing the squared error, so we need the derivative of the trace of , with respect to ,

## Slide 69
Here, another miracle happens...

## Slide 71: Ganho
Measurement uncertainty
State uncertainty in the prediction

## Slide 72
Kalman gain for
Kalman gain for
What is the effect of this?

## Slide 73
The residual would be and the position/velocity estimate would not change.
If the position estimate were the same as the measurement…

## Slide 74
The prediction was very different from the measurement, , so the position and velocity values are updated.
If the position estimate was really bad…

## Slide 75
The greater the correlation, the greater the speed correction.
The higher, the greater the correction, as the more reliable the measurement is in relation to the prediction.
If the position estimate was really bad…

## Slide 76
PREDICT
UPDATE

## Slide 77
dt = 1.
R_var = 10
Q_var = 0.01
x = np.array([[10.0, 3.0]]).T
P = np.diag([500, 1])
F = np.array([[1, dt],
[0, 1]])
H = np.array([[1., 0.]])
R = np.array([[R_var]])
Q = Q_discrete_white_noise(dim=2, dt=dt, var=Q_var)
Input data for our filter

## Slide 78
count = 50
track, zs = compute_robot_data(R_var, Q_var, count)
xs, cov = [], []
for z in zs:
# predict
x = F @ x
P = F @ P @ F.T + Q
#update
S = H @ P @ H.T + R
K = P @ H.T @ np.linalg.inv(S)
y = z - H @ x
x += K @ y
P = P - K @ H @ P
xs.append(x)
cov.append(P)
xs, cov = np.array(xs), np.array(cov)
plot_track(xs[:, 0], track, zs, cov, plot_P=False)
Movement
simulation
Prediction
Update
Data storage update
vectors with new
state and cov.

## Slide 80
from filterpy.kalman import KalmanFilter
Poli_filter = KalmanFilter(dim_x=2, dim_z=1)
print('x = ', Poli_filter.x.T)
print('R = ', Poli_filter.R)
print('Q = \n', Poli_filter.Q)
# etc...
Creation of the Robot
Poli
x = [[0. 0.]]
R = [[1.]]
Q = [[1. 0.]
[0. 1.]]

## Slide 81
from filterpy.kalman import KalmanFilter
from filterpy.common import Q_discrete_white_noise
def pos_vel_filter(x, P, R, Q=0., dt=1.0):
""" Returns a KalmanFilter which implements a
constant velocity model for a state [x dx].T
"""
kf = KalmanFilter(dim_x=2, dim_z=1)
kf.x = np.array([x[0], x[1]]) # location and velocity
kf.F = np.array([[1., dt],
[0., 1.]]) # state transition matrix
kf.H = np.array([[1., 0]]) # Measurement function
kf.R *= R # measurement uncertainty
if np.isscalar(P):
kf.P *= P # covariance matrix
else:
kf.P[:] = P # [:] makes deep copy
if np.isscalar(Q):
kf.Q = Q_discrete_white_noise(dim=2, dt=dt, var=Q)
else:
kf.Q[:] = Q
return kf
Instancie o filtro
Set correct values for matrices and vectors.

## Slide 82
def run(x0=(0.,0.), P=500, R=0, Q=0, dt=1.0,track=None, zs=None,
count=0, do_plot=True, **kwargs):
"""
track is the actual position of the robor, zs are the
corresponding measurements.
"""
# Simulate robot if no data provided.
if zs is None:
track, zs = compute_robot_data(R, Q, count)
# create the Kalman filter
kf = pos_vel_filter(x0, R=R, P=P, Q=Q, dt=dt)
# run the kalman filter and store the results
xs, cov = [], []
for z in zs:
kf.predict()
kf.update(z)
xs.append(kf.x)
cov.append(kf.P)
xs, cov = np.array(xs), np.array(cov)
if do_plot:
plot_track(xs[:, 0], track, zs, cov, **kwargs)
return xs, cov
Check whether measurement data in zs has been provided. Otherwise, create the data using our compute_robot_data..
create the Kalman filter
perform the Kalman filter update and prediction steps for each measurement
Plot the results, then return the saved states and covariances

## Slide 86
There is still a lot to learn, but we have implemented a Kalman filter using the same theory and equations published by Rudolf Kalman! Code much like this runs inside your GPS, airplanes, robots, and so on.

## Slide 87
Hands on
Simple exercises, not mandatory, but they will provide the necessary knowledge for the filter... In short: if I were you, I would do them...

## Slide 88: Adjusting the filter
Consider that our robot has real values of measurement variance and process variance To see the effects of measurement noise and process noise , the following exercises are proposed :
for a constant measurement variance of 200 (constantat a very large value will serve to magnify the effects of various design choices on the graphs, making it easier to recognize what is happening), test the process variances of and ;
With the actual process and measurement variance values, change the initial position to 50 and the initial velocity to 1 to see how the filter behaves with a poor initial estimate;
set the process variation to 0.2 , and increase the measurement variation to 10000 ;
With the data defined as in item 3, change the initial position to 50 𝑚 and the initial velocity to 1 𝑚/𝑠 to see how the filter will behave with a bad initial estimate.

## Slide 93: Homework 01 (optional)
For the path measured by the GPS shown in the figure below, use the Kalman filter and trace the trajectory of the vehicle.
Use the variance data and initial estimates defined in the Notebook.

## Slide 94: EKT: Extended Kalman Filter
It's not all sunshine and roses…

## Slide 95: Kalman Filter theory
The Kalman filter theory proposed by R. Kalman has two strong assumptions:
  The Kalman Filter will always work with Gaussian Distribution;
  The Kalman Filter will always work with Linear Functions.
What if my function is no longer linear? The solution is to make them linear by approximation. After applying the approximation, what we get is an Extended Kalman Filter, or EKF.
In EKF, the transition models (which define the matrix F) and state observation (which define the matrix H) do not need to be linear functions of the state, but can be differentiable functions.

## Slide 97
O-ho. Most real-world problems involve nonlinear functions. For example, in many cases, the system is looking in one direction and taking measurements in another direction. This involves angles and sine and cosine functions, which are non-linear functions...

## Slide 98
Prediction:
Correction:

## Slide 99: Your challenge...
where is the angle with the horizontal axis and is the angular velocity. The Lagrangian derivation of the simple pendulum equations of motion yields:
Where
A gyroscope detects angular velocity .

## Slide 100: Simulation of the real behavior of the pendulum and the measurement process
def dynamics_evolution(x, u):
'''
returns the new state i+1, given the previous state i added to random process noise q
'''
return A.dot(x) + B*(-np.cos(x[0])*m*g*l-c*x[1] + u + np.random.normal(0,np.sqrt(q)))
def measurement(x):
'''
returns measurement added to random sensor noise r
'''
return x[1] + np.random.normal(0,np.sqrt(r))
Pendulum movement
Speed measurement

## Slide 101: Class Observer
class Observer():
def __init__(self, initial_state, initial_covariance):
self._xb = np.array(initial_state)
self._xh = np.array(initial_state)
self._Pb = np.array(initial_covariance)
self._Ph = np.array(initial_covariance)
def FMatrix(self, state):
pass
def prediction(self, u):
pass
def correction(self, z):
pass
def predicted_corrected(self):
return self._xh
Check the preservation of the initial nomenclature x bar, x hat.
Your homework

## Slide 102
Inverted pendulum
Without control, verification of the real movement of the pendulum
Control using the actual position of the pendulum as feedback
Without control, verification of the pendulum movement from the perspective of the Kalman Filter (process+sensor)
Control using Kalman filter feedback

## Slide 103
Inverted pendulum
Without control, verification of the real movement of the pendulum
Control using the actual position of the pendulum as feedback
Without control, verification of the pendulum movement from the perspective of the Kalman Filter (process+sensor)
Control using Kalman filter feedback

## Slide 104: CONTROL Class Control_Empty()
class Control_Empty():
def __init__(self):
pass
def observe(self, x, z):
return np.zeros(2)
def action(self):
return 0
Uncontrolled system (like our robot).
The pendulum is free, starting from the position π/2 and then descending.

## Slide 106
Inverted pendulum
Without control, verification of the real movement of the pendulum
Control using the actual position of the pendulum as feedback
Without control, verification of the pendulum movement from the perspective of the Kalman Filter (process+sensor)
Control using Kalman filter feedback

## Slide 107: CONTROL CLASS: Control_PIDwithState()
class Control_PIDwithState():
def __init__(self, kp, kd):
self._kp = kp
self._kd = kd
def observe(self, x, z):
self._state = x
return x
def action(self):
return self._kp*(np.pi/2-self._state[0])-self._kd*self._state[1]
Observed state is exactly the real state of the system.
PID control

## Slide 109
Inverted pendulum
Without control, verification of the real movement of the pendulum
Control using the actual position of the pendulum as feedback
Without control, verification of the pendulum movement from the perspective of the Kalman Filter (process+sensor)
Control using Kalman filter feedback

## Slide 110: Control class: Control_EmptyWithObserver()
class Control_EmptyWithObserver():
def __init__(self, initial_state, initial_covariance):
self._observer = Observer(initial_state, initial_covariance)
self._last_action = 0
def observe(self, x, z):
self._observer.prediction(self._last_action)
self._observer.correction(z)
return self._observer.predicted_corrected()
def action(self):
return 0
Observed state is Kalman result
Uncontrolled...

## Slide 112
Inverted pendulum
Without control, verification of the real movement of the pendulum
Control using the actual position of the pendulum as feedback
Without control, verification of the pendulum movement from the perspective of the Kalman Filter (process+sensor)
Control using Kalman filter feedback

## Slide 113: Control Class: Control_PIDwithObserver()
class Control_PIDwithObserver():
def __init__(self, kp, kd, initial_state, initial_covariance):
self._observer = Observer(initial_state, initial_covariance)
self._last_action = 0
self._kp = kp
self._kd = kd
def observe(self, x, z):
self._observer.prediction(self._last_action)
self._observer.correction(z)
return self._observer.predicted_corrected()
def action(self):
state = self._observer.predicted_corrected()
self._last_action = self._kp*(np.pi/2 - state[0]) - self._kd*state[1]
return self._last_action
Observed state is Kalman result
Control...

## Slide 115: simulation
def simulation(x0, controller):
x = x0
z = measurement(x)
prediction = controller.observe(x, z)
u = controller.action()
yield z, u, x, prediction
while True:
x = dynamics_evolution(x, u)
prediction = controller.observe(x, z)
u = controller.action()
z = measurement(x)
yield z, u, x, prediction
Initial values of state (x0), measurement (z), Kalman prediction (prediction) and control (u)
Evolution for each new state until simulation of N time intervals.

## Slide 116: Let's try to use what we learned...
outputs = []
states = []
predictions = []
actions = []
for z, u, x, e in list(itertools.islice(simulation(np.array([np.pi/2 - 0.1, 0]), Control_Empty()), 10000)):
outputs.append(z)
states.append(x)
actions.append(u)
predictions.append(e)
outputs = np.array(outputs)
states = np.array(states)
actions = np.array(actions)
predictions = np.array(predictions)
plt.plot(states[:,0])
plt.plot(outputs[:,0]);

## Slide 117: homework 02
Block Diagram: There will be a designated area in Moodle for submitting your block diagram as an image (JPEG or PNG).
Coding Task: Complete the code to generate the results demonstrated in class.

## Slide 118: FIM